## Slide 1: Voltage Fields
A Simple Parallel Programming Exercise

## Slide 2: Problem Statement
Cross section of rectangular metal tube
Sides insulated from each other
(not connected)
VB = 0.0 volts
VT
VL
VR
Problem: Compute voltage at interior points
Each side at a different voltage

## Slide 3: Approach
VB = 0.0 volts
VT
VL
VR
(0, 0)
x
y
Compute Voltage at each mesh point

## Slide 4: Details at Each Point
V[x, y]
V[x+1, y]
V[x-1, y]
V[x, y-1]
V[x, y+1]
V[x, y] = (V[x+1, y] + V[x, y+1] + V[x-1, y] + V[x, y-1]) / 4.0
Voltage is average of surrounding mesh points

## Slide 5: Method
Use a two dimensional array of double
  Initialize the “edges” to the side voltages
  Initialize the interior to 0.0
Sweep over interior only and update each point to be average of adjacent points
Repeat until results converge on a solution

## Slide 6: Notes
Results more accurate with a fine mesh
  … but larger number of points increases computation time
  An example of time/accuracy trade-off!
How many iterations over the interior are necessary?
  Until no point changes more than δ percent? (for some small δ)
  It’s not obvious that is correct. Consider the harmonic series
    1 + 1/2 + 1/3 + 1/4 + … diverges even though the terms approach zero
  Nevertheless we’ll use this approach for now!